## Slide 1
Unit – II
Industrial Productions
Mr. S. N. Mendhe
Department of Microbiology,
Shri Shivaji Science and Arts College, Chikhli

## Slide 2
Industrial Production of
Citric Acid
Citric acid occurs naturally as a component of many fruits.
In 1784, Scheele isolated the citric acid for the first time from lemon juice and crystallized as a solid.
Before the development of fermentation technology, the citric acid was obtained by the extraction from juices of certain citrus fruits (lemon) and later from pineapple waste.

## Slide 3
Today, most of the commercial citric acid is obtained from microbial fermentation process. Critic acid is used in many fields.
Some important industrial uses of citric acid are as follows :
Critic acid is used as an acidulant in foods in pharmaceutical industries (e.g. jams, preserved fruits, fruit drink).
Critic acid is used as a chelating and sequestering agent (e.g. in the tanning of animal skin).
It is also used in the production of carbonated beverages as a preservative and flavor enhancer.

## Slide 4
  Critic acid is used in the manufacture of soft drink to which citric acid gives the cool taste.
  The citrate and citrate esters are used as plasticizers.
Manufacture of Citric Acid:
There are various fermentation processes used in the manufacture of citric acid.
These are:
Surface culture method
Submerged culture method
Solid state fermentation

## Slide 5
Production of citric acid by surface
culture method
In this method, the culture is inoculated across the surface of production media and culture remains on the surface throughout the fermentation.
This is an old process and it is still practiced. The process includes:-
Microorganisms
Preparation of Inoculum
Preparation of Fermentation Medium
  Fermentation Conditions
  Recovery

## Slide 6
  Microorganisms:
  Large number of fungi produce citric acid from sugar e.g. Aspergillus niger, Aspergillus clavatus, Penicillum species and Mucor species but in these some fungi produces small yield, some produces undesirable substances and some shows undesirable characteristics, so these are undesirable for the commercial production.

## Slide 7
Only some selected strains of Aspergillus niger are used for the commercial production because of following reasons:-
They are high yielding or efficient strains.
They posses stable biochemical characteristics.
They produce negligible amount of other acids such as oxalic acid, gluconic acid, malic acid etc.
They can be easily cultivated.

## Slide 8
Preparation of Inoculum:
Spores of Aspergillus niger are used to inoculate fermentation media.
Spores of Aspergillus niger strains are produced by growing a fungus on a suitable solid sporulation medium at 25⁰C for 4 to 14 days.
The suspension of spores is prepared by suspending the grown spores in suitable diluents, such as water.

## Slide 9
Preparation of Fermentation Medium:
The selection of favorable fermentation medium is important in obtaining high level of citric acid by the Aspergillus niger.
Sucrose is the best source of carbon among the various sugars as it gives maximum yield of citric acid.
Fructose and glucose gives lower yields of citric acid. However, sucrose concentration above 15% should not be used because the excess amount of sugar remains unconverted to citric acid.

## Slide 10
Beet molasses is extensively used as a raw material for the commercial production of citric acid. Beet molasses requires pre-treatment, since it contains excessive amount of trace metals.
These metals affect citric acid production. Therefore, it is necessary to minimize the concentration of these metals in the fermentation media.
For this beet molasses is treated with potassium before sterilization. Apart from carbohydrates, other trace elements namely potassium, phosphorus, sulphur, magnesium are to be added in the fermentation media

## Slide 11
These metals are added in the form of their salts.
According to Currie (1917), the most favorable fermentation media for producing citric acid contains following compounds:-
Sucrose - 125 to 150 gm. /lit
Ammonium nitrate - 2 to 2.5 gm. /lit
KH2PO4 - 0.75 to 1 gm. /lit
MgSO4.7H2O - 0.20 to 0.25 gm. /lit
pH - 3.4 to 3.5
Inorganic salts should not be added beyond the concentration mentioned above otherwise yield of citric acid is lowered.

## Slide 12
Fermentation Process:
Fermentations are carried out in shallow pans made up of aluminum of purity of 99.80% or greater. In the citric acid fermentation, the conversion of sugar to citric acid is brought about by the intracellular enzymes.
Sugar is metabolized by the molds and citric acid is excreted outside in the medium.
Therefore, citric acid fermentation is advantageous in shallow pans where the medium is covered by a thin layer of mycelium mat and is rapid rather than deep tanks, in which the surface area of mycelium is small in comparison to the volume to the medium.

## Slide 13
In shallow pans, a large surface area of the mycelium is exposed to a relatively shallow layer of fermentation media.
Under such conditions, high level of the sugar is converted to citric acid and moreover fermentation is rapid and fermentation time is shortened.
In shallow pans, fermentation medium is inoculated by blowing the spores across the surface of the medium so that they float in the medium.
For obtaining maximum yields, following fermentation conditions should be maintained.

## Slide 14
pH: The low pH values (3.4 to 3.5) are favorable for the citric acid production. Use of low pH is advantageous because
High yield of citric acid is favored and oxalic acid production is suppressed.
Danger of contamination is minimized.
iii) Best citric acid producing molds possess greatest tolerance to low pH values.
Low pH is adjusted by the addition of HCl only. Other acids like H2SO4, Nitric acid and acetic acid can be used for pH adjustment but are inferior to HCl.

## Slide 15
Temperature: A temperature range of 26 to 28⁰C is considered to be satisfactory and increase in temperature above 30⁰C decrease the citric acid yield.
Aeration: The citric acid fermentation is essentially an aerobic fermentation and organism needs abundant supply of oxygen for growth. Therefore, it is necessary to supply sterile air.
Agitation: Agitation of the fermentation medium is not required as gentle or moderate shaking under surface culture conditions decrease the citric acid production.

## Slide 16
Time: The fermentation process is usually completed within 7-10 days.
Yield: 60 to 80 gm. of citric acid/100 gm. of sugar is produced in surface culture method.
Recovery of Citric Acid:
The citric acid is recovered from the fermented broth as follows:
At the completion of fermentation, the solution is drained off and mycelial mat is pressed to remove any citric acid contained in it.

## Slide 17
Solution is treated with calcium carbonate to form the precipitate of calcium citrate.
The precipitate of calcium citrate is filtered and washed. The calcium citrate precipitate is then treated with an equivalent amount of sulphuric acid.
In this treatment the citric acid is separated and calcium is removed as a precipitate of calcium sulphate.
The precipitate of calcium sulphate is separated by the filtration and impure solution of citric acid is obtained.

## Slide 18
Colour impurities present in impure citric acid solution is removed by treating the impure citric acid solution with activated carbon which absorbs the impurities and give citric acid solution.
Finally, the pure citric acid solution is concentrated and is crystallized from the solution.